## Slide 1: Bridging the Gap: Preparing your Jurisdiction for Civil unrest
Copyright 2025: National Association of State Fire Marshals

## Slide 2: Acknowledgements
This program was made possible by a grant from the Federal Emergency Management Agency’s (FEMA), Assistance to Firefighters Grant Program, Award EMW-2021-FP-00833 under Fiscal Year (FY) 2021.
NASFM would like to take this opportunity to thank not only FEMA, but all those who helped to prepare this program together.

## Slide 3: Introduction

## Slide 4: Introduction
Guidance Document
Prevention perspective
Two types of discussion
Regulatory
Best Practices
Additional References
Several other references are available
Notes: This project is intended to provide guidance to fire departments that wish to develop plans related to any type of civil unrest that may affect the communities they serve. Specifically, we will consider planning from a fire prevention perspective as opposed to an operational or response viewpoint. As in almost any risk related issue, prevention can pay significant dividends - in this case in the form of reduced damage, reduced injuries and enhanced firefighter safety. Our goal is to offer suggestions that will enhance your community’s overall safety by utilizing design, business operation, and informational ideas to reduce the opportunity for offenders to damage property through vandalism and fire setting. We will include both regulatory criteria, which may be required, as well as recommendations for businesses that may not be required, but would be useful to reduce damage during an event.
Several other reference documents are available through the on-line training program at http://nasfm-training.org

## Slide 5: Key points
Have a plan
Exercise the plan
  Tabletop
  Full scale
Work the plan (before, during and after)
Modify the plan based on experience
Notes: Ultimately local jurisdictions, including prevention personnel, need to have a plan in place before an event, even for prevention personnel to follow in advance of such an event occurring. Such plans should be exercised on a regular basis with adjustments based on local needs and experiences. When exercising the plan, start with a tabletop event and then proceed to full scale exercises to identify any issues needing to be addressed (keep in mind that full scale exercises may cause stress in the local community). While each jurisdiction is will be different based upon a number of local factors, this program will help bring many items to your attention when developing a plan. This includes items prevention and inspection personnel can do in their daily activities.

## Slide 6: Definition and Examples
Definition
Civil unrest means the gathering of more than one person, in reaction to an event, with the intention of causing a public disturbance inclusive of violent protests or disorder (excluding peaceful demonstrations), riots, arson, looting, occupation of institutional buildings, border infringements and armed insurrection in violation of the law.
Events
January 6, 2021 – Washington DC – Election related
May 26, 2020 – Minneapolis, MN – George Floyd Protests
April 2016, - February 2017 – Dakota Access Pipeline Protests
Keys
Planning
Mitigation
Communication
Notes: You may be asking, “what kinds of events are we talking about here?” One definition of civil unrest is: “Civil unrest means the gathering of more than one person, in reaction to an event, with the intention of causing a public disturbance inclusive of violent protests or disorder (excluding peaceful demonstrations), riots, arson, looting, occupation of institutional buildings, border infringements and armed insurrection in violation of the law.” The most recent examples of civil unrest in the U.S. includes recent violent protests in response to deaths and injuries inflicted by law enforcement, an attack on the U.S. Capitol in response to claims of election fraud, and various acts of violence in response to significant victories by sports teams. All of these can be predicted to some extent, and therefore planning should result in mitigation of some or all the potential damage.
While not scientific research, current estimates have listed nearly 500 incidents of civil unrest and subsequent riots in the United States alone since its founding.

## Slide 7: A Necessary Paradigm Shift
Change in the thought process of the inspector
Normally inspectors look for a particular risk profile
  Accidental Fires
Inspectors should be including the possibility of Civil Unrest at they are conducting business
  Ask different questions
  Include the potential for criminal activity
Modern Fire and Building Codes can be a guide
Notes: A beneficial change that can assist in preventing damage from these events is a modification of the thought process used by inspectors when assessing a property. Normally, fire inspectors and fire marshals assess properties using a risk profile linked to the potential for an accidental fire.
In order to successfully prepare for the kind of event we’re considering, an inspector will need to include these potential events in their thought processes. This simple change will cause the inspector to ask different questions, suggest different solutions, and, in general, expand the inspection to include criminal activity. While most regulations (including fire codes) don’t focus on criminal behavior as a rule, there are many criteria in modern fire and building codes that will, if applied, help safeguard properties from vandals and others intending to do harm to the building.

## Slide 8: Build Your Communications Network
YOUR AGENCY
Text
Social Media
AFFECTED PUBLIC
OTHERS
Email
Phone
Targeted Correspondence
Reverse 911
RESPONDERS
You are here
Notes: Probably the most important item in our toolbox for reducing risk during civil unrest is a robust communications pipeline to deliver and receive information in the timeliest manner possible. The system should provide contact information for all of the commercial occupancies in the jurisdiction. Electronic correspondence – text or email – is the quickest and most dependable way to get information to your community. If the system allows targeting by geographic location, pertinent information can be distributed to only those affected, and reduce the chances of “information overload” that often occurs during a crisis. There are commercial systems available that allow the user to select recipients based upon various parameters such as location, size of building/business, etc. It’s worth considering the procurement of such a system if one isn’t already available; they can be used for weather alerts, crime alerts, and various other events that occur in every community. This paper is primarily focusing on commercial buildings, but these systems are invaluable for notifying residences of changing conditions as well. The systems are useful for law enforcement, emergency management, utilities, etc. to notify citizens and customers of important information. That said, if the system is shared, a comprehensive understanding of how it is to be utilized and who makes decisions about outgoing messages should be established when the system is acquired.
CLASSROOM Exercise: Brainstorm all the ways you can potentially communicate an issue involving civil unrest.

## Slide 9: Communications and Building Relationships
Trash Collection
Public Works
Heavy Equipment Operators
Construction Companies
Private Security Companies
Parks and Recreation
Mutual Aid Resources
Improve relations with other organizations
Notes: In addition to communicating with those outside government agencies, it’s advantageous to have close relationships with those agencies (public and private) we may not associate with on a regular basis. If an event is pending, trash collection could be stepped up to remove trash receptacles in the affected area; public works equipment and personnel could be utilized to clear construction sites of loose debris and materials; and heavy equipment can be used to barricade streets or facilities. Think through your own jurisdiction and potential resources to enhance your response to prevent damage.

## Slide 10: Working together
Public
Fire
Law Enforcement
EMS
Public Works
Private
Affected public
Development Organizations
Private interest groups
Others
Notes: We would be remiss if we didn’t mention the need for close coordination between public safety agencies, public works and other government agencies, as well as private groups that can be impacted by an event. Maintaining good relationships is important under any circumstances, but during a true community crisis, there is no room for any discord of any kind. Clear communications, unified command, and assigned responsibilities will pay big dividends to the public we serve.
In class questionnaire: Who else or what other organization could we add to these lists?
Potential classroom exercise: Decide who has final decision about message content to Chamber of Commerce, Public Alerts and news media. Public Officials? PIO? Law Enforcement? Fire Department? Management? Emergency Services?

## Slide 11: Strategies
Notes: Now let's discuss some specific strategies

## Slide 12: Sprinkler Systems
40 percent of businesses never reopen after a fire
Value of Sprinklers
25% of new businesses fail in the first year after a fire
40% of businesses never reopen after a fire
Civil unrest
During incidents, most buildings with active sprinklers survive these event, while many without are destroyed.
Deterrent
Anecdotal evidence indicates sprinklers deter looters.
Notes: We all realize the value of sprinkler systems in reducing fire loss in our communities. According to the Insurance Information Institute (iii.org), forty percent of businesses never reopen after a fire, and an additional 25 percent fail within one year of reopening. It’s likely that the statistics for businesses burned in a civil disturbance will be even worse, as the rebuilding of the community involves much more than bricks and mortar.
We have considerable experience over the last several years with various types of civil disturbances where those creating the disturbance decide to set fire to buildings in an area. In those cases, it has been documented that most buildings with active sprinkler systems survived the attempted arsons, while many of the buildings without sprinklers were destroyed. While sprinklers aren’t necessarily designed for an arson fire, they have performed well in recent outbreaks. Most of the data is anecdotal, but those who attended the fires have reported high success rates in mitigating a fire event where sprinklers were present. Another observation has been that, when a sprinkler system activates, it’s a significant deterrent to looters and others who may want to commit crimes in the building. It’s probably more difficult to operate in a building with water pouring out of the sprinklers than it is in a dry environment – and the odor and appearance of the initial sprinkler discharge isn’t pleasant.

## Slide 13: Fire protection systems
Asses the system
  Is it maintained in accordance with adopted codes and standards
Types of Systems Available
  Hood Systems
  Special Hazard Systems
  Fire Alarms
  Portable Extinguishers
If an event is imminent or pending, a final “sweep” of businesses in the target area may be in order to be sure systems are maintained, are in working order and secured.
Routine Inspections
Notes: Any routine fire inspection includes an assessment of any fire protection systems installed on the premises. Checking to see systems have been inspected and maintained in accordance with adopted standards is important to ensure they will operate as designed should a fire occur. This includes sprinkler systems, kitchen hood systems, special hazard systems, fire alarm systems and portable fire extinguishers. Typically, all of these will have a tag installed by a service technician that will indicate the status of the system or device, along with the date the system was last checked. If an event is imminent or pending, a final “sweep” of businesses in the target area may be in order to be sure systems are maintained and secured.
901.4.1 Required fire protection and life safety systems.
Fire protection and life safety systems required by this code, or the International Building Code shall be installed, repaired, operated, tested and maintained in accordance with this code.

## Slide 14: Special Considerations
Occupancy Changes or building changes
  Permanent
  Temporary
  Emergency
Building Construction
Building design or layout changes
Hand Sanitizer
  Now installed in numerous locations
  Can be 80% alcohol
  Large storage quantities a possibility
    Potential fire hazard
Notes: Sometimes overlooked are changes to the occupancy or the building. Because each system is designed to a specific risk (hazard), any changes to the contents or the building could render the fire protection unreliable. For instance, over the last several years, hand sanitizer has become ubiquitous in our society. Virtually every office, store, or other occupancy has hand sanitizer available to employees and customers. It’s easy to overlook the fact that this material is highly flammable – up to 80% alcohol is routine. So, while a small personal container of the liquid may not present a significant risk, storage of pallets of the material may present a challenge that the sprinkler system wasn’t designed to address. Because the risk of fire setting is heightened during civil unrest, it’s important to confirm the sprinklers, extinguishers, etc. are appropriate for the risk.
In classroom, discuss other possible items that can fall into this category (renovations, Hazardous materials storage, etc.)

## Slide 15: Vacant Buildings
Attractive Targets
Permanent or Seasonal
Status of the buildings systems
Have changes been approved
  Revocation of approvals
Notes: Vacant buildings present an attractive target for criminals, especially during civil disturbances. Under some circumstances, systems in these buildings are permitted by most codes to be modified or taken out of service due to potential freezing or other conditions. These policies and procedures are worth revisiting to be sure that the jurisdiction isn’t creating a target for arsonists unnecessarily. If there is a high risk of civil unrest, previous approvals to take systems out of service may be worth consideration. Consideration should be given to the time and nature of building vacancy, and to the overall condition of vacant properties. For example, buildings which are vacated for a short duration due to seasonal uses or changes of tenants or ownership, may have more complete protection systems in place that could be used during times of vacancy. Where the automatic water supplies to internal fire sprinkler or standpipe systems have been shut off during periods of building vacancy, water could be supplied to operate these systems by reopening closed control valves or providing required water supplies through fire department connections which are connected to the system on the system side of control valves.
SECTION311
VACANT PREMISES
311.2.2 Fire protection.
Fire protection systems shall be maintained in an operable condition at all times.
(Exceptions excluded from this text)
International Fire Code, 2021 Edition

## Slide 16: Securing and Monitoring Protection Systems
Requirement
Consideration
Best Practice
Consideration should also be given to physically securing control valves for sprinkler systems.
Physical securing of valves isn’t a requirement of the model codes but should be considered as a policy change to the adopted regulations when deemed necessary
Monitoring must be maintained
Notes: There are specific requirements for securing or monitoring fire protection systems in both the fire codes and related standards. While monitoring of systems is important, and will provide notification of activation or closed valves, consideration should also be given to physically securing control valves for sprinkler systems. If a chain and lock is installed to keep a valve open, it will add considerably to the degree of difficulty for someone attempting to shut the system down if they want to prevent automatic control or suppression of incendiary fires. The physical securing of valves isn’t a requirement of the model codes (IFC or NFPA) but should be considered by the local jurisdiction as a policy change or potential amendment to the adopted regulations when deemed necessary.
903.4 Sprinkler system supervision and alarms.
Valves controlling the water supply for automatic sprinkler systems, pumps, tanks, water levels and temperatures, critical air pressures and waterflow switches on all sprinkler systems shall be electrically supervised by a listed fire alarm control unit.
(Exceptions excluded from this text)
International Fire Code, 2021 Edition

## Slide 17: Sprinkler Controls
Code requirements
  Several are to provide access to responders
Additional Considerations
  Civil unrest causes disruptions
  Balanced approach
  Keep unauthorized personnel from shutting valves
Notes: There are several code requirements intended to provide access to valves and controls by responding fire fighters; this is so that water supplies can be easily shut off during an emergency and reduce water damage. When considering disruptions like civil unrest, there is value in considering a balanced approach whereby unauthorized personnel are prevented from easily shutting valves that could keep the system from operating.
30.4.12.2 Alarm signals shall be provided for, but not limited to, each of the following: monitoring position of control valves, fire pump power supplies and operating condition, water tank levels and temperatures, zone waterflow alarms, pressure of tanks, and air pressure on dry pipe valves.
NFPA 13, 2019 Edition

## Slide 18: Fire Department Connections
Often a target for sabotage due to
  size and ease of access
Easily removed
Inspect and flush as able
Consideration should be made for
  the use of locking caps
Notes: Fire department connections are important to assure sprinkler and standpipe systems receive the necessary support from responding fire fighters when needed. Unfortunately, these are particularly vulnerable to vandalism; the size of a two-and-a-half-inch inlet is almost exactly the size needed to accommodate a soda or beer can, and for some reason people tend to stuff trash and other debris into FDC’s that don’t have their caps intact. (During one event, a Molotov cocktail was found inserted into an FDC). Screw-on caps have been the norm until recently, when plastic break-away caps became popular because they’re inexpensive to replace. The problem is that these are also easily removed when someone wants to sabotage the fire protection system. One answer is to install locking caps on the FDC. While they’re more expensive than the plastic caps, they shouldn’t have to be replaced because they’re locked on, and only the fire department has a key to unlock them. The fire code provides the fire code official with the authority to require locking caps, so this is an option for jurisdictions wishing to assure they are properly secured. Note that protection of dry standpipes is of paramount importance because they don’t have an automatic water supply and depend solely on the fire department for supplying water in most cases.
To prevent vandalism in buildings, and to preserve the ability of a standpipe to operate, consideration should be given to requiring locking caps on standpipe outlets as well as the FDC’s. This is addressed in the IFC as well.
912.4.1Locking fire department connection caps.
The fire code official is authorized to require locking caps on fire department connections for water-based fire protection systems where the responding fire department carries appropriate key wrenches for removal.
International Fire Code, 2021 Edition

## Slide 19: Monitoring Systems
Requirement
Consideration
What if?
Wireless or Hard-wired?
Will the wireless work if the cellular system is overwhelmed?
Verification of operating status
Notes: During any assessment of a fire protection system, any monitoring arrangement should be verified by contacting the monitoring agency and confirming they are receiving the appropriate signals being sent by the various devices (trouble signals for electrical failures; supervisory signals for mechanical failures, and alarm signals for emergency conditions water flow, etc.). It should be noted here, however, that during major crises, it isn’t unusual for wireless communications (cell phone systems) to become overloaded to the point they can’t provide dependable service. If monitoring systems are utilizing the wireless option, it’s possible, even likely, that they will not be able to transmit signals to their respective monitoring agencies during a significant event.

## Slide 20: Security Measures
Notes: In today’s society, many communities are facing rising crime rates, necessitating more substantial hardening of facilities that are targets of criminals. When contemplating civil disturbance activities, the need for more robust security measures takes on even greater importance for business owners. As people contemplate the potential loss of their property and livelihoods, they can become very innovative in finding ways to provide protection. Sometimes, their schemes aren’t well thought out and create greater risks.
1010.2Door operations.
Except as specifically permitted by this section, egress doors shall be readily openable from the egress side without the use of a key or special knowledge or effort.
International Fire Code, 2021 Edition

## Slide 21: Security Devices
Codes intent is for people to exit without any special knowledge, tools or effort
Any modification which impedes egress is likely illegal
If possible, modifications should be
  Removed
  Modified to allow unimpeded egress
Makeshift locking devices should be prohibited
Notes: While there are exceptions for certain types of occupancies (detention centers, certain health care occupancies, psychiatric facilities, etc.), the fire and building codes intend for people to be able to exit any building they’re in without special knowledge, tools, or effort. Any security device that impedes egress by locking, barricading or otherwise blocking a person from exiting the building should be carefully evaluated and, where possible, removed or modified so that exiting isn’t affected. For instance, if building is equipped with revolving doors, and the emergency egress consists of folding (collapsing) those doors to provide unimpeded egress to the outside, then installing plywood on them will probably defeat the emergency egress feature and should be reconsidered. On the other hand, if the revolving doors have normal swinging doors adjacent to them, plywood may be an option.
Makeshift locks and locking devices, padlocks and hasps, barricades and similar solutions are almost always prohibited on exit doors. When found, they should immediately be removed or modified so that egress isn’t affected.
1032.2Reliability.
Required exit accesses, exits and exit discharges shall be continuously maintained free from obstructions or impediments to full instant use in the case of fire or other emergency where the building area served by the means of egress is occupied. An exit or exit passageway shall not be used for any purpose that interferes with a means of egress.
1032.2.1Security devices and egress locks.
Security devices affecting means of egress shall be subject to approval of the fire code official. Security devices and locking arrangements in the means of egress that restrict, control, or delay egress shall be installed and maintained as required by this chapter.
International Fire Code, 2021 Edition

## Slide 22: Panic Hardware
Door-latching assembly incorporating a device that releases the latch upon the application of a force in the direction of egress travel
Definition
Propping open to permit later entrance
Criminal Activity
Are they working properly
Are they installed properly
Are they being blocked or propped open
Checks
Maintain in a closed position
Monitor in advance
Notes: According to the International Fire Code, panic hardware is a door-latching assembly incorporating a device that releases the latch upon the application of a force in the direction of egress travel. This type of hardware is required on most exit doors installed in public assembly and educational occupancies and is common in some others. Panic hardware is designed to permit a person to exit a building without turning a doorknob, releasing a latch, or any other action that could possibly slow down or impede the flow of people from the building. They can still be secured, as the hardware can be arranged to latch when the door closes, effectively locking people out of the building but allowing those inside to exit in an emergency. Unfortunately, when this type of hardware isn’t installed properly or is damaged or worn through normal use, the latching mechanism may not work as designed. In these cases, some building owners and operators choose to add other locks to the doors rather than replace or repair the panic hardware. This is a violation that should be rectified immediately upon discovery.
Sometimes, an employee or customer may use a rock or other device to prop a door with panic hardware open so that they can reenter the building – the person may want to go outside to smoke or to visit with someone and reenter the door they exited. In other situations, a criminal may prop a door open to keep the panic hardware from latching so that they may enter the building later for nefarious purposes; this is what occurred at a mass shooting at a movie theatre in Aurora, Colorado. If a business has doors equipped with panic hardware, it’s valuable to monitor them closely – especially in times of civil unrest - to be sure that doors can be secured when closed.

## Slide 23: Magnetic Locking Systems
May provide better security than mechanical locks
Regular inspection and maintenance
Require Power
Do Battery backups work
  Regularly checked
In case of failure or power outage
  Install Mechanical lock
  Physical monitoring
Notes: One option to traditional locking devices is a magnetic locking system. If listed “mag locks” are installed properly, they may offer better security than traditional mechanical locking devices and systems. However, these systems require power to maintain the doors in a locked condition; power failure will cause the lock to release. Because of this, it’s beneficial to monitor the power source to the door and to be prepared to take appropriate measures if power is lost. Even if the system has a battery backup to the system, if power is off for an extended length of time, the battery will fail, and the lock will release. Appropriate measures would likely include the installation of a mechanical locking device, and physically monitoring the door to assure egress is maintained.
This is a good time to point out that backup power may not be reliable unless regularly checked; this is true not only for power door locks, but also other systems, such as fire alarm and monitoring systems.
1010.2.11Door hardware release of electrically locked egress doors.
Door hardware release of electric locking systems shall be permitted on doors in the means of egress in any occupancy except Group H where installed and operated in accordance with all of the following:
1. 1.The door hardware that is affixed to the door leaf has an obvious method of operation that is readily operated under all lighting conditions.
2. 2.The door hardware is capable of being operated with one hand and shall comply with Section 1010.2.1.
3. 3.Operation of the door hardware directly interrupts the power to the electric lock and unlocks the door immediately.
4. 4.Loss of power to the electric locking system automatically unlocks the door.
5. 5.Where panic or fire exit hardware is required by Section 1010.2.9, operation of the panic or fire exit hardware also releases the electric lock.
6. 6.The locking system units shall be listed in accordance with UL 294.
International Fire Code, 2021 Edition

## Slide 24: After Hours
Must egress be maintained after hours?
  Codes recognize the need for security after hours
  Egress systems shall be maintained when the area served is occupied
  Maintain impediment free egress systems
    Note: Security Personnel
Notes: A common question about locking buildings is whether egress must be maintained after hours if the building isn’t occupied. The codes recognize the need for security, especially when the building is empty; thus, it has language that states that the egress system shall be maintained when the area served is occupied (emphasis added). The next question is typically “what about skeleton crews or stocking crews, etc. that are in the building after hours? In those cases, the occupied area must have access to compliant means of egress. It’s likely that some jurisdictions will allow exceptions for security personnel making their rounds to check that the building is secured, but beyond that, the exceptions to maintaining an impediment-free egress system are rare.
Note that NFPA 101 provides guidance about when to consider a building occupied under its chapter on office buildings. According to that guidance, if it’s after hours, and there are less than 10 persons in the building, it isn’t considered to be occupied and can be secured.
1032.2Reliability.
Required exit accesses, exits and exit discharges shall be continuously maintained free from obstructions or impediments to full instant use in the case of fire or other emergency where the building area served by the means of egress is occupied. An exit or exit passageway shall not be used for any purpose that interferes with a means of egress.
International Fire Code, 2021 Edition

## Slide 25: Firefighter Safety
Owners and occupants may create their own security devices
  Booby traps
  Firearms
  Pitfalls
All are strictly prohibited by the fire code
  The fire code calls them pitfalls
IFC 2021 Edition 316.3 Pitfalls
  The intentional design or alteration of buildings to disable, injure, maim or kill intruders is prohibited.
Notes: Paramount in any discussion about fire prevention should be fire fighter safety. And, while all of our previous suggestions and recommendations have been intended to enhance the safety of responders, we should point out here that there are some owners and occupants that will attempt to create their own security devices, sometimes creating significant risks to anyone except those that installed the devices. Consider a firearm that is aimed at a door and rigged to fire if the door opens, injuring or killing the intruder – or responding fire fighter. Other “booby-traps” have been found to include axes, cross bows, and other weapons arranged to fall or be propelled toward a door. These arrangements are strictly prohibited by the fire code; they’re called pitfalls in the code and are described below.
316.3Pitfalls.
The intentional design or alteration of buildings to disable, injure, maim or kill intruders is prohibited. A person shall not install and use firearms, sharp or pointed objects, razor wire, explosives, flammable or combustible liquid containers, or dispensers containing highly toxic, toxic, irritant or other hazardous materials in a manner that could passively or actively disable, injure, maim or kill a fire fighter who forcibly enters a building for the purpose of controlling or extinguishing a fire, rescuing trapped occupants or rendering other emergency assistance.
International Fire Code, 2021 Edition

## Slide 26: Security Systems
Cannot emit a medium that would obscure a means of egress
  Filling a space with smoke
  Intent to confuse intruders
Unintended Consequences
Notes: Additionally, the codes prohibit any security system that emits a medium that could obscure a means of egress; this was in response to a company that was marketing a security system that, when triggered, filled the protected space with smoke. Their intent was to confuse the intruders and obscure their escape until law enforcement could arrive. Obviously, these systems had unintended consequences and were eventually prohibited by the model fire codes.

## Slide 27: USE of Plywood
Should never interfere with egress
Will obscure visual observation
Should never cover FDCs
How will plywood impact the business if it is operating.
In areas of severe weather, consider the placement of hurricane shutters or impact resistant windows during construction.
Fire retardant plywood is available and should be considered for buildings with rated exteriors.
Notes: Finally, no discussion about securing buildings during an emergency would be complete without a discussion about the use of plywood to cover windows, doors and other openings. As anyone who has ever seen a community prepare for civil disturbances or severe weather knows, plywood seems to be the “go to” material for securing buildings. It is widely available and relatively inexpensive. Covering windows and glass doors with plywood can, many times, save thousands of dollars in damage from rock-throwers or wind-blown debris. There are dozens of websites with instructions on how to board up openings, and few, if any, consider egress or fire fighter access in their advice. It is worth considering a checklist or other hand-out to business owners that wish to use plywood for securing their businesses; some of the issues are:
• In areas subject to severe weather, such as hurricanes, many buildings will be equipped with hurricane shutters or impact resistant (hurricane) windows. In these cases, the use of plywood isn’t necessary.
• Plywood should never interfere with egress from a space
• Plywood will obscure visual observation, both from inside and outside the space; is this an issue for the business?
• Plywood should never cover fire department connections
• Fire retardant plywood is available and should be considered for buildings that have rated exterior walls
• Consider how plywood will impact the business if it is operating with the plywood in place

## Slide 28: Outside the Building

## Slide 29: Location of Trash Containers
Code
Restrict large trash containers such as dumpsters from being within five feet of the exterior of the building (IFC 304.3.3)
Recommendation
Discuss the best location with the owner and helping the owner understand the risk to the property that comes from dumpster fires
Other Considerations
Placed well away from building
If it has wheels, make it immobile
Lock the lid if possible
Place in a secure area
Empty before planned events or protest
Remove if possible
Place in an area out of sight
Notes: The fire codes restrict large trash containers such as dumpsters from being within five feet of the exterior of the building (IFC 304.3.3); however, when determining the appropriate location of a dumpster if planning for civil unrest, it’s best to discuss the best location with the owner and helping the owner understand the risk to the property that comes from dumpster fires. Dumpsters are particularly attractive to those prone to violence. If the dumpster has wheels, consider making it immobile to that it can’t easily be moved close to the building; if it has a way to lock the lid to prevent access, keep it locked; if it is in a secured area behind non-combustible walls, make sure the area is secured against unwanted entry. Finally, if possible, have the dumpsters emptied before any planned protest or event, and consider removing the dumpster from the premises for the duration of the event.

## Slide 30: Landscape Considerations
Consider the arson and civil unrest threat
High oil content plants may exacerbate fires
Combustible mulch next to combustible cladding should be removed or replaced
Artificial plants
  Combustible vs. noncombustible
  If combustible, they are prohibited within 5 feet of the exterior in certain conditions
Seasonal decorations
  Removed
  Restricted as noted for artificial plants
Notes: For other than wildland urban interface areas, landscaping has largely gone unaddressed in the fire codes; however, when considering arson and civil unrest, it’s worth taking a look. We know that plants with a high moisture content are difficult to ignite and burn slowly, so those plants should be promoted in our communities, as we never really know when civil unrest may occur. Plants with high oil content may exacerbate any small exterior fire and, if they’re planted in close proximity to building openings, may cause an exterior fire to extend inside the structure.
Combustible mulch can also be a consideration, especially if it’s adjacent to combustible exterior cladding on the building. It is recommended that owners be advised to either remove such mulch before any contemplated event or replace it permanently with noncombustible material.
Some businesses use large artificial plants outside their buildings. If these are not combustible, they don’t present a fire risk. However, if they are combustible (plastic, cloth, etc.), the IFC prohibits such plants over six feet in height within five feet of the exterior of the building unless they meet specific flame spread criteria. (IFC 321.1). This should also apply to outdoor displays that present similar risks.

## Slide 31: Buildings under construction
Notes: When considering widespread or localized civil unrest, building under construction are a major factor from two perspectives:
1. Buildings under construction provide an extraordinarily attractive target to those wishing to do harm; they are easily ignited and difficult to extinguish
2. Construction sites typically contain many unsecured items that can be utilized by rioters or arsonists.

## Slide 32: Security Consideration
Fencing
Security systems
On Site personnel
Site Assessments
Fire Safety Provisions
Notes: In order to prepare a construction site for potential civil unrest, we can start with security.

## Slide 33: Fencing
Withstand Daily abuse
Min 6’ in height
Topped with wire
Gates should be robust
Secured
Maintained
Notes: Almost every job site should be fenced. While the fencing is typically temporary, it should be installed to withstand the daily abuse it will experience on a construction site. It should be at least 6- feet tall, and consideration should be given to lining the top with barbed wire or razor wire. (Note that local authorities should be consulted about the wire, as some have regulations about placing a “hazard” on the top of the fence.) Gates in the fencing should be robust, as they’ll get a lot of use during construction. They should be able to be secured without leaving space for someone to crawl through the opening.

## Slide 34: Security Systems
Monitored alarm systems should be in place
Video monitoring
Cameras
Signage indicate its presence
Notes: In addition to fencing, many sites could benefit from an appropriate security system. Gates, storage buildings, jobsite offices and other buildings may be equipped with security alarm systems to notify authorities should someone attempt to break in. In addition to the electronic monitoring, consideration should be given to video monitoring of critical areas of the site. Video cameras, along with appropriate signs stating that the monitoring is present can be a powerful deterrent.

## Slide 35: Security Personnel
Fire Watch
Security Patrol
Notification of Authorities
Plans should include triggers
  When to evacuate
  Safe evacuation routes
  Shelter or protect in place strategies
Note: Recommendation to avoid direct confrontation with violent demonstrators
Notes: Finally, an on-site security presence may be suitable. Security personnel can serve as both a fire watch and security patrol, which will achieve a bit of savings for the owner. Security personnel will typically notify the proper authorities and avoid direct confrontation with violent demonstrators. Plans for security personnel should include appropriate triggers for them to evacuate, and safe evacuation routes or “protect in place” strategies.

## Slide 36: Site Assessment
Secure tools and loose equipment
Remove heavy equipment from the site
Loose building materials(bricks and lumber) should be removed.
Roofing torches, plumber’s torches and any other tools that could be used to easily ignite combustible materials should be removed
Maintain a constant water supply to the site.
If fuel is stored on site, it should be removed or moved to a safe location.
Notes: In addition to securing the site, an assessment should be undertaken to identify building materials, tools and equipment that violent demonstrators would be expected to use to harm the site or other buildings and people in the area. Heavy equipment should be removed from the site, as criminals can do substantial damage with loaders, bull dozers and similar equipment – not to mention that the loss of this equipment would add considerably to the financial loss in any event. Roofing torches, plumber’s torches and any other tools that could be used to easily ignite combustible materials should be removed from the site for obvious reasons. Building materials that can be used for throwing at windows or authorities should be removed from the site if possible; bricks, stone, steel rebar, and lumber all make potent weapons in an engagement between the law breakers and authorities. Finally, if fuel is stored on the property in portable tanks or cans, they should be removed to a safe location.
Of course, all of the other fire safety provisions should be maintained at these sites – water supply, fire department access, compliance with the site safety plan, etc. are all features that will make the site safer during any kind of civil disturbance.

## Slide 37: Additional Resource
Bridging the Gap: Construction Site Fire Safety
https://www.firemarshals.org
Notes: A NASFM publication, “Bridging the Gap: Construction Site Fire Safety” has a copious amount of information to help identify issues related to construction sites and the fire risk they present. The publication, is accompanied by a comprehensive on-line and in-person training program; for information and access to the information, go to: https://www.firemarshals.org/Construction-Site-Fire-Safety.

## Slide 38: When an Event Appears Imminent
Notes: Much of what’s been discussed up to this point has been routine preparation that can be incorporated into normal inspection processes. However, when an event is imminent, or when the potential for disturbances is high, an elevated response is necessary to prevent as much damage as possible.

## Slide 39: Know What you can do
Laws
Rules
Statutes
Ordinances
Codes
Standards
Emergency Orders
Notes: First and foremost, we must know the state laws and rules that may be contemplated, especially if a state of emergency is declared. Each state’s laws are different, and we need to fully understand what changes may be implemented under an emergency declaration and what cannot be changed under such orders. Your jurisdiction’s legal staff should be able to outline any potential opportunities or roadblocks that come with an emergency declaration. Once we have a clear understanding of our authority, we can begin working to prevent damage to our community.
Fire and Building officials must do their homework and research the specific laws, rules, statutes, ordinances, emergency orders and even zoning regulations that will come into play in their jurisdictions.

## Slide 40: Fire Codes
102.9Matters not provided for
  Requirements essential for public safety….shall be determined by the fire code official
IFC 102.9
Where there are practical difficulties involved in carrying out the provisions of this code, the fire code official shall have the authority to grant modifications for individual cases……..
[A] 104.9Modifications.
The provisions of this code are not intended to prevent the installation of any material or to prohibit any design or method of construction not specifically prescribed by this code……..
104.10 Alternative materials, design and methods of construction and equipment.
Notes: This is also a good time to revisit some fire code provisions that are intended to provide flexibility to the code official:
102.9Matters not provided for.
Requirements that are essential for the public safety of an existing or proposed activity, building or structure, or for the safety of the occupants thereof, that are not specifically provided for by this code, shall be determined by the fire code official.
[A]104.9Modifications.
Where there are practical difficulties involved in carrying out the provisions of this code, the fire code official shall have the authority to grant modifications for individual cases, provided that the fire code official shall first find that special individual reason makes the strict letter of this code impractical, and the modification is in compliance with the intent and purpose of this code and that such modification does not lessen health, life and fire safety requirements. The details of action granting modifications shall be recorded and entered in the files of the department of fire prevention.
104.10Alternative materials, design and methods of construction and equipment.
The provisions of this code are not intended to prevent the installation of any material or to prohibit any design or method of construction not specifically prescribed by this code, provided that any such alternative has been approved. An alternative material, design or method of construction shall be approved where the fire code official finds that the proposed design is satisfactory and complies with the intent of the provisions of this code, and that the material, method or work offered is, for the purpose intended, not less than the equivalent of that prescribed in this code in quality, strength, effectiveness, fire resistance, durability and safety. Where the alternative material, design or method of construction is not approved, the fire code official shall respond in writing, stating the reasons why the alternative was not approved
International Fire Code, 2021 Edition

## Slide 41: Outside the box
These code provisions may be utilized to allow enhanced security due to an impending event
They don’t require the code official to accept any condition that is found objectionable
Owners may have safe solutions that may not be in strict compliance
Document, document, document
Develop statutes and ordinances in advance that grant authority during civil unrest
Notes: These code provisions may be utilized to allow enhanced security due to an impending event; they don’t require the code official to accept any condition that is found objectionable, but if an owner or occupant has an innovative approach that may not be in strict compliance, these sections will allow the approval of alternatives based upon the enhanced risk associated with a civil disturbance. It’s always advisable to document any decisions made in this regard.
Another option for consideration is to develop statutes (ordinances) that provide for enhanced authority during a civil emergency to require business owners to take actions such as trash removal, dumpster relocation or removal, clear construction sites and similar measures to reduce the risk of property damage.

## Slide 42: Working with Law enforcement
Prior to and during the event
Information gathering
  Social media
  Other Sources
Fusion Centers
Can guide area of Greatest risk
Notes: In many cases in the past, (probably most cases), demonstrations began peacefully and escalated into violence. A march or a demonstration will likely be planned, so the location of the event is known. If this isn’t the case, it’s likely that law enforcement will be monitoring activity on various social media platforms and will be gathering data from informants and others in an attempt to predict where potential violence may occur. With this information, the fire prevention officials can focus on businesses, residences, construction sites, etc. in the area of greatest risk. At this point, your department has hopefully developed plans and procedures to communicate with the business community about how to best protect their property.

## Slide 43: Work the Plan
Large events
Potential for violence
Controversial issues
Activate your communication system
What's the potential
What areas may be impacted
Timelines
Follow their plan
Distribute pre-made checklists and guides
Communicate with the business community
Premade communication groups and methods
Organize with decision makers
Plan ahead
Notes: As soon as there is a sign of impending civil disturbance, your communications system should be activated – it may be that a big sports event in your community is scheduled, and the event could spur violence by revelers; it could be that a local arrest or other action has angered your community and marches or protests are scheduled; or it could be an event on the other side of the country, a trial verdict or other event that spurs people in your community to protest and possibly riot. Regardless of the catalyst, have your instructions to your business community ready to go out over your communications system at the earliest opportunity. Provide all appropriate information about the potential for violence and vandalism, the geographic area affected, and timeline if there is one. Remind business owners to follow their plan, and if checklists are available, include those in your notification if possible. In addition to sending status reports and recommendations to implement their plans, a request for any pertinent information from the recipients should be made. Setting up a group to receive this information, organize it and share it with other agencies can help decision makers who need to allocate resources and make other important decisions in response to actions by those creating the civil disturbance.
NOTE: Consideration of activating your Emergency Operations Center and staffing it with appropriate personnel from various agencies is appropriate ahead of any potential event.

## Slide 44: After the event
Notes: If your jurisdiction experiences a severe civil disturbance event, it’s likely that widespread damage will occur. This will be an opportunity to determine how well your plan worked, and what changes need to be made to your plan. Sharing your experiences with other jurisdictions will help them better prepare for such an event.
Was your intelligence accurate? What was missed?
Do you think the level of property damage was reduced as a result of your efforts at risk reduction?
Were there any issues with compliance ?
Were your codes, standards and statutes enough to provide for your community?

## Slide 45: Assessments
Determine the overall damage
Level of need from state and federal resources
Activate business continuity plans
Aid in recovery
Similar to weather related plans
Notes: As with any event causing major damage, an assessment should be conducted. This assessment will be important to determine the level of assistance needed from state and federal authorities. In addition, it will be an opportunity to interface with the business community to help them recover as quickly as possible, and to reduce any risks that may result from temporary or unpermitted repairs and construction.
In reality, the damage assessment component of your plan can probably be copied from your weather-related disaster plan, as recovery from damage from a man-made disaster will not be that different from recovery from damage due to natural disaster.

## Slide 46: Summary
Have the plan
Work the plan (even during daily activities)
Have communication strategies that incorporate everyone
Work together
Think outside the box but provide for safety first
Notes: Every community should have a plan to address civil disturbances and the fire department should be an integral part of the planning process. Working to prevent damage from a civil disturbance can pay significant dividends for your community by preserving buildings that might otherwise perish during riots. If businesses can reopen soon after an event, the entire community benefits. When it appears that an event is imminent, it’s too late to plan; it needs to be done now.
The plans should begin with a communications strategy that incorporates all jurisdictional agencies, commercial property owners and operators and citizens. The communications tool used should be able to reach any component of the community (residential/commercial, etc.) and should be able to make notifications based upon geographic locations. These systems are available commercially and can be shared by all agencies in a jurisdiction. They can even be shared between jurisdictions where appropriate.
Inspectors and other staff should be familiar with the plan and any collateral that your agency develops that can be used to educate the business community (checklists are very helpful). The thought process associated with hardening facilities should be incorporated into routine inspections and discussed with the business owners during these visits. These discussions are much easier to have before any threat is imminent; free and open exchanges of ideas will help everyone if the unthinkable occurs in your community.
The suggestions and guidelines contained herein should help your jurisdiction prepare for an event in a manner that focuses on preventing damage to your community.

## Slide 47: THANK YOU
National Association of State Fire Marshals
www.firemarshals.org